#### Affordable water solutions

Jal-TARA Chloroscope

Description

Determination of chlorine is required to confirm that water is safe for drinking purpose from bacterial contamination. Therefore residual Chlorine testing in chlorine treated water at supply end and at household become important. Chlorine demand optimization and its quantity (dose) fixation during water treatment process is also a necessary process where residual chlorine monitoring is regular need.

In market there is hardly any good quality affordable and reliable Chloroscope is available for residual chorine (RC) content testing in disinfected water. Development Alternatives has designed and developed a device named Jal-TARA Chloroscope to determine residual chlorine (RC) in disinfected water by application of chlorine based substance. It test is colorimetric visual comparison method. With this device anyone can check effectiveness of treatment of water (RC) in field where chlorine based disinfectants have been used for this purpose at very low rate.

Product package has been made ready and launched at commercial platforms for benefits of people. Public Health Departments, Water Testing Labs, Swimming pools, Hotels, Clubs, Industrial Labs, Sanitary staff and Individuals engaged in drinking water disinfection using chlorine are using this kit for quick check chlorine contents in water. Couple of minutes requires to conduct the test.

Advantages

- Robust, fast and easy to operate, can be used in field and on-site

- Reagents are dry and safe in use. Easy to carry

- One kit performs up to 100 tests

- Reagent refill set is also available

- Long shelf life of over 1 year

- Attractive designed device to test residual chlorine on-site

- Test range 0.0, 0.2,0.5,1.0,3.0,5.0 mg/L residual chlorine

Current Status

The technology has been fully adopted and is being commercially disseminated. Knowledge products including user manual and brochures are available for Jal-TARA Chloroscope to test the presence of residual chlorine in the drinking water. So far 250 kits have been commercially made available to clients. Customized training packages are available for health centres, foundations, water quality monitoring labs and NGO.

# Text boxes

Jal -TARA Chloroscope in two different packaging boxes